## Slide 1: Conveyor belts automation
Course: Programmable controllers for Industrial Automation
Student: Savev David

## Slide 2: Assignment
Goal: “Automation of a conveyor belt system by using a Programmable controller”

## Slide 3: I/O devices
Input devices:
Start, Stop, Reset button (N.O. pushbuttons);
Emerg. switch (N.C. switch);
Proximity sensor (N.O. of inductive type);
3 Photocells (Laser diode + phototransistor);
3 thermic contacts of the motors (N.O);
Output devices:
3 monophase motors with moto-reducers;
24V operation light (green) and emergency light (red).
TOTAL: 11 digital inputs, 5 digital outputs.

## Slide 4: Operational states
We can extract the following states out of the system requirements: Idle, Wait, Operative, Emergency.
We can associate to the states the digital outputs of the system:

## Slide 5: Main state machine
Developed in Ladder Diagram, sub-divided into two different blocks: ActiveStateMachine and ErrorStateMachine
Emergency status was split into 3 to maintain reference to previous state.

## Slide 6: Variables
The following global variables were declared:
IOVars (1:1 mapping with the physical I/O devices);
GlobalVars (taking into account states and internal variables).

## Slide 7: Functions and FB
Following functions and function blocks were declared to increase the maintainability, readability and re-usability of the code:
OverHeating (Function in ST): logical OR combination of the motor thermostats;
ObjectCounter (FB in ST): controls the number of objects on the conveyor belts by using 3 up-down counters, 3 global int linked to the belts (countLine1, countLine2, countLine3) and 1 other global int as result of the sum of the previous three (countTotal).;
Delay (FB in ST): delays the off switching of the motors by a ϑ constant through the usage of a TOFF timer;
Multivibrator (FB in ST): provides a PWM signal with a configurable duty cycle in order to manage the blinking of the red light.

## Slide 8: ObjectCounter

## Slide 9: Output control
OutputActive and OutputEmergency were developed in Ladder Diagram in order to control the actuators (motors and lights); the high-level structure is the following:

## Slide 10: Hardware considerations
To standardize the working logic of the photocell receivers, it is more logical to have:
HIGH SIGNAL = BEAM INTERRUPTED = OBJECT DETECTION;
LOW SIGNAL = BEAM PRESENT = OBJECT ABSENCE.
I decided to use at the receiver side a pull-up configuration for the phototransistor:

## Slide 11: PLC selection
The Logic controller that was selected is the Zelio Logic Smart Relay SR3B261BD selled by Schneider electric.
Supply voltage: 24V DC;
16 input ports (10 digital and 6 analog/digital);
10 relay-based output ports supporting a quite large current (8A or 5A).
Chosen since it is the cheapest (232 euro) and since has enough input/output ports to control the system without the need of expansion modules.

## Slide 12: Electric circuit

## Slide 13: Final considerations
Optimization by using one single digital input for the motor thermostats by basically connecting them in a series configuration;
We are relying to much on the photocells. What if a phototransistor is faulty? Triple-Modular Redudancy circuit uses 3 blocks instead of one and in case of one faulty photocell can decide the correct output based on the working two.